## Slide 1: CLIMATE RESILIENCE SUPPORT FOR KENYA WATER, SANITATION, AND HYGIENE PROGRAM (K-WASH)
Mainstreaming Climate Resilience into WASH Projects – Case Studies
18th December 2025

## Slide 2: Contents
01.
Objectives of the CRA
02.
Benefits of Mainstreaming Climate Resilience in WASH
04.
Understanding Climatology, Physical Parameters & Hazards
05.
Hazard & Investment Mapping
06.
Adaptation Options
Challenges we Encountered
07.
03.
CRA Process
Lessons Learnt
08.

## Slide 3: 01. Objectives of the CRA
        What is a Climate Risk Assessment ? What is the purpose of a Climate Risk Assessment ?
        Climate risk assessments identify the likelihood of future climate hazards and their potential impacts on communities. This is fundamental for informing the prioritization of climate action and investment in adaptation.
        In this case the CRA informed CWSSIP to ensure investment planning ensures adaptation through:
        Climate proofing of investments
        Due consideration of climate change when choosing investments location

## Slide 4: 02. Benefits of Mainstreaming Climate Resilience in WASH
Reduces operation and maintenance costs of water and sanitation infrastructure by minimizing climate-related damage and failures.
Improves efficiency in the use of financial resources, allowing savings to be redirected toward service expansion and increased coverage.
Promotes the development of durable, climate-resilient WASH infrastructure that can reliably serve current and future generations.

## Slide 5: 03. CRA Process
CRA steps
          STEP 1) Understanding the climatology and physical parameters
          STEP 2) Identifying hazards and exposure to it
          Consider past events and current exposure
          Account for climate change impacts on exposure
          STEP 3) Understanding vulnerability to hazards to which the County is exposed
          Especially WSS sectoral vulnerability
          Social and sectoral vulnerability
      Human Health
      Agriculture
      Coastal zone
      Energy and infrastructure
      Ecosystems
      Disproportionately impacted groups
          Transversal : Mapping and analyzing each step

## Slide 6: 04. Understanding Climatology, Physical Parameters & Hazards
        Parameters & Hazards Associated to Climate Change
Water

## Slide 7: 04. Understanding Climatology, Physical Parameters & Hazards
Understanding existing risks & their evolution with climate change
          Current Climatology Historical trends Projections
Observed annual average precipitation (top) and mean surface air temperature in Tana River
Source : CCKP
Monthly climatology, 1991-2023; Tana River
Source : CCKP
Projections of average mean temperature under SSP5-8.5
Source : CCKP
Frequency, intensity, duration &
locale of occurrence

## Slide 8: Hazard Identified
Tana River
Floods:
  Heavy rainfall floods (All county)
  River floods (Tana River surroundings mainly)
  Rising water table floods (limited information to map this out – surroundings on Tana River)
Heat stress and droughts (all the county)
Coastal erosion (coastal area) and rustle erosion (all the county)
Soil and water salinity (coastal area and irrigated inland areas or one close to rivers)
Sand and dust storms (all the county)
Pest and diseases (all the county)

## Slide 9: Hazard Identified
Murang’a
Floods:
  Maragua & Kiharu – intakes submerged, high treatment costs, 20–40% households affected
Drought:
  Severe in Ithanga/Kakuzi – up to 50% households affected; long treks for water, crop loss.
Landslides
  Frequent in Kangema, Mathioya, Kigumo – 2025 landslide in Kangema killed 6, cut off 980 HHs.
Extreme Rainfall
  Ndaka-ini station recorded 1,355 mm (among Kenya’s highest seasonal totals).
Heat Stress:
  Outdoor workers & water pans/dams affected by evaporation and heat waves.

## Slide 10: Murang’a Temperature

## Slide 11: Murang’a Drought

## Slide 12: Landslides

## Slide 13: Land Use Cover Change

## Slide 14: Pluvial floods

## Slide 15: 05. Hazard & Investment Mapping
          Importance of Mapping
HAZARDS
INVESTMENTS

## Slide 16: 05. Hazard & Investment Mapping – Landslide hazard

## Slide 17: 06. Adaptation Options
Based on field visits, litterature review (good practices) and experts’ inputs adaptation options were identified at three levels:
Project Design
County Level – Programmes and Legislation
Community Level Adaptation Practices

## Slide 18
Climate hazard | Impacts on infrastructure & Service quality | Impacts on environment and water resources | Social impact | CWSSIPs investments concerned | Adaptation Measures
Drought | Cracking of Linings: (e.g. with clay) Poor Water Quality (Salinity) Water Shortage | Degradation of resource quality through reduced dilution of pollutants Reduced Water Levels - Lack of Recharge: Loss of biodiversity | Disruption of Livelihoods: - water for Irrigation, livestock or domestic use Water resource conflicts between communities Health Risks – disease outbreaks | Construction of Bilbil water pan project in Chewele ward Construction of a new dam, construction of a slt trap, construction of auxilliary works, construction of a draw-off system, construction of a perimeter fence and a VIP toilet | Design considerations – Deepening to increase depth to boost storage capacity while reducing evaporation exposure Desilting - reduce evaporation exposure. Planting trees along the banks of the water pan – provide shade cover
Intense and sudden rainfall, flooding | Submergence of Pump and Headwork's Damage: - failure of pumps and other electrical systems rendering out of service out of service Submergence of boreholes – Water Contamination Reduced Accessibility Increased Maintenance Costs | Aquifer Pollution and Recharge Issues Loss of Biodiversity | Community Displacement Loss of human lives Disease outbreak – : waterborne diseases – cholera, typhoid, dysentery | Construction of Kaniki water supply project in Galedertu SC- The construction works will involve hydrological survey at Kanini village, Drilling and equipping of 2No. Boreholes, 1No. 50cum capacity elevate steel water tank at Gurujo, HDPE PN12 Rising main from kaniki to Gurujo and 2No. Standard water kiosks (1no. Per village). | Elevated Borehole Platforms –raised concrete plinths to protect borehole headworks and pump systems from floodwaters. Solar-Powered Pumps – reduce reliance on diesel pumps (fossil fuel)
Landslides | ………. |  |  |  | 
          Water Supply Infrastructure Table

## Slide 19: 06. Adaptation Options – Design adaptation examples
Elevated Borehole Platforms
HDPE water supply pipes with electro-fused joints ensures a watertight system.
Solarization of boreholes
Elevated storage tank enables gravity-fed water distribution - minimizing maintenance costs
Concrete reinforced pit latrines
Construction of ladder-like steps at designated water collection points along the River Tana to facilitate safer an easier water fetching.
Building fitted with gutters to harvest rainwater
Reinforced concrete water pipe anchors
Underground water pipelines

## Slide 20: 06. Adaptation Options – Design adaptation examples
Elevated Borehole Platforms – Madogo Tana River
Solarization
Adaptation to water transportation over long distances - Wolestokocha
Elevated Water Tanks

## Slide 21: 06. Adaptation Options – Design adaptation examples
HDPE pipes anchored by reinforced concrete –Irate, Murang’a

## Slide 22: 06. Adaptation Options – Design adaptation examples
Relocated pipes running along River South Mathioya valley in Kiarathe with river crossing fitted with GI pipes from the joint chambers and firmly anchored by concrete reinforced anchors

## Slide 23: 06. Adaptation Options – Design adaptation examples
Operational sheets for each investments are generated based on their location and their related hazard exposure, it lists all the adaptation that could be relevant for the proposed investment.

## Slide 24: 06. Adaptation Options – Programmes and Legislation examples
Construction of WASH infrastructure:
  Drilling boreholes
  Construction of Water Pans and Dams
  Water Supply network extension
Maintenance of existing water infrastructure
Enforcing proper design of dams, water structures, ensure compliance of engineering design standards and regulations.
Prevention and sensitization against encroachment of riparian areas, slope management by advocating for terrace farming, agroforestry, afforestation and tree planting
County Government supplements community efforts by distributing water treatment agents such as Pur and Aqualam.

## Slide 25: 06. Adaptation Options – Programmes and Legislation examples
Adaptation goes beyond the infrastructure – it includes legislation and other programmes at county-led programmes
Slope Stabilization – Murang’a
Need for Slope Management – Terrace Farming Practices - Afforestation – Tree Planting

## Slide 26: 06. Adaptation Options – Programmes and Legislation examples
Agroforestry – Kiarathe, Murang’a
Slope Management - Afforestation – Tree Planting

## Slide 27: 06. Adaptation Options – Community level adaptation practices examples
Planting trees
Roof water harvesting
Soil conservation
Pastoralism
Planting drought resistant crops
Boiling of drinking and traditional water treatment

## Slide 28: 07. Challenges We Encountered
Absence of most WSP representatives limited accurate identification of investment locations, as counties could only provide general, non-specific site information.
Mixing technical officers and community representatives in joint discussions reduced community participation, as technical staff dominated the conversations.
Some counties did not nominate the intended CWSSIP technical officers, necessitating additional training for backend teams to ensure continuity and institutional learning

## Slide 29: 08. Lessons Learnt
Active participation of Water Service Provider (WSP) representatives was critical as they implement most CWSSIP projects for some counties. Their involvement improves the accuracy of hotspot identification and investment locations.
Mapping investment locations was essential for identifying site-specific adaptation measures aligned to the climate hazards affecting each locality.
Separating technical discussions from community consultations, while ensuring complementarity between the two, leads to more inclusive, practical, and actionable outcomes.
Counties that engaged GIS Officers, Climate Change Officers, and Water Officers showed stronger technical understanding and ownership. Future support should prioritize early and consistent involvement of all relevant technical staff

## Slide 30: Contact
Romain VIAVANT
Team Leader
romain.viavant@groupehuit.com
Emma GUILLOT
Project Coordinator
emma.guillot@groupehuit.com
Paul OKECH
Stakeholder engagement expert
okechpol@gmail.com
Nelson KISANYA
GIS Mapping Expert
nelsonkisanya2010@gmail.com
+ 254 704 170888
+ 254 706 092688