## Slide 1: Toolkit for Water and Sanitation Infrastructure Planning
MODULE 5
Notes: Facilitators notes:
This module is designed to equip participants with the knowledge and tools needed to understand and manage the impacts of climate change on water and sanitation
infrastructure.
Exercise: Guiding principles for participation
At the start of each day, remind the participants of these simple ‘housekeeping’ principles:
Listen carefully, follow along and make your own notes.
Ask the trainers questions or clarifications at any time.
Your own experience is valuable, and we encourage you to share it.
Share and discuss with others during exercises, breaks and reflections.

## Slide 2
01 | Overview Module 5 Including Learning objectives
Practical toolboxes for reviewing infrastructure systems | 
02 | Defining infrastructure systems
03 | Toolkit for water infrastructure planning (the climate adaptation matrix)
04 | Case study – climate first tool
 | LUNCH
A Paradigm shift: scenario-based planning for future infrastructure | 
05 | What is scenario-based planning?
06 | Practical exercises
07 | A quiz & end of the day reflection
go.mwater.co/irc/2025_kenya
All information of this course
Notes: Facilitators notes:
Overview of the main content of this presentation.
Here’s our roadmap for the day. We'll start by defining what we mean by infrastructure systems, then dive into a practical toolkit for planning, including a case study.
After lunch, we'll explore a crucial mindsetshift: scenario-based planning. We'll also discuss how to work with limited data and the practicalities of tendering out a climate risk
assessment.
We'll finish with a quiz and a reflection to consolidate your learning.

## Slide 3
Acknowledgements
We would like to acknowledge the following partners and funders involved in designing and delivering the Climate Resilient Water Services Masterclass:
The Modules were developed with
Notes: Facilitators notes:
Here you can acknowledge who contributed to the development of the Masterclass.
We would like to acknowledge the following partners and funders involved in designing and delivering the Climate Resilient Water Services Masterclass (CRWSMC).

## Slide 4: Our river
Our river is living in a human influenced environment– with bridges, river embarkments and dams.
Photo by Rejaul Karim on Unsplash
Notes: Facilitators notes:
As combining theme though the course, we will use the metaphor of a river. Each day will be represented by a part of the river.
Discuss with colleagues how adaptations are made . What are the dams/blockages in achieving resilience? How can we create space for rivers/adaptation? What tools do we have
to make the river flow?

## Slide 5
01| Overview Module 5
Photo by Ivan Bandura on Unsplash
Notes: Facilitators notes:
Let's begin with a high-level overview of what this module is all about.

## Slide 6
Online introduction
Module 2
Climate Risk Assessments
Climate hazards & risks and the role of inclusion
Climate Adaptation and Resilience Options
Toolkit for water and sanitation infrastructure planning
Module 3
Module 4
Module 5
Module 1
Equips participants to understand and manage the impacts of climate change on infrastructure.
Notes: Facilitators notes:
This module is designed to equip participants with the knowledge and tools needed to understand and manage the impacts of climate change on water and sanitation infrastructure.
To reorient us, remember that Module 5 builds directly on everything we've learned. Module 1 gave us the foundation, Module 2 the concepts of resilience, Module 3 the risk assessment process, and Module 4 the adaptation options. Now, Module 5 equips you to integrate all of that into concrete infrastructure planning

## Slide 7: Module 5 toolkit for water and sanitation infrastructure planning
This module covers:
Scenario-based planning approaches
Climate stress testing of water infrastructure
Adaptation options
Foundations of infrastructure management
Duration: 1 day
Notes: Facilitators notes:
This slide provides a summary of what will be taught in Module 5:
This module is designed to equip participants with the knowledge and tools needed to understand and manage the impacts of climate change on water and sanitation
infrastructure.
It covers:
Scenario-based planning approaches to assess and manage the effects of climate change on infrastructure functionality and long-term planning needs (scenario-based planning)
Climate stress testing of water infrastructure using appropriate tools and methodologies, including rapid assessment techniques (climate first tool).
Foundations of infrastructure management, including:
  Differentiating between hard and soft infrastructure
  Applying systems thinking to address complex challenges
  Selecting and adapting suitable solutions across diverse contexts

## Slide 8
Learning objectives
Notes: Facilitators notes:
Here are today's learning objectives.

## Slide 9: Module 5 learning objectives
By the end of this module, participants will be able to:
Apply a structured and context-sensitive approach to infrastructure planning and resilience-building in the face of climate uncertainty.
Understand climate change impacts on infrastructure systems
Differentiate between hard and soft infrastructure components
Apply scenario-based approaches to climate resilience planning
Conduct rapid stress tests for water infrastructure systems
Develop integrated adaptation strategies for various contexts
Notes: Facilitators notes:
This slide provides a summary of what will be taught in Module 5:
This module is designed to give participants a structured approach to building resilient infrastructure in a changing climate. The key learning objectives are to help them
understand climate impacts, distinguish between hard and soft infrastructure, use scenario-based planning, and stress-test water systems. By the end, they should be able to
develop integrated adaptation strategies for their own contexts.
Read these objectives aloud. Emphasize the action verbs: 'apply,' 'differentiate,' 'conduct.' This isn't just about knowledge; it's about building practical skills.

## Slide 10
Practical toolboxes for reviewing infrastructure systems
Notes: Facilitators notes:
We will go into detail in our module, starting with the first part, namely Practical toolboxes for reviewing infrastructure systems

## Slide 11
03 | Nature-based Solutions
Nature-based solutions can complement, substitute for, or protect traditional grey infrastructure to enhance the resilience of service delivery to climate change.
Complement: Restoring watersheds, which serve as ecological infrastructure supplying water to reservoirs, plays a vital role in regulating hydrological processes and maintaining water quality.
Substitute: Using deep-rooted vegetation for slope stabilization offers a cost-effective alternative to building concrete retaining walls, and is estimated to save up to 90% in implementation costs.
Safeguard: Afforesting mangrove forests could protect shorelines from erosion, thus safeguarding nearby roads, buildings, and utilities from wave damage during storms and sea surges.
Notes: Trainer Notes:

## Slide 12: Contents
01.
Objectives of the CRA
02.
Benefits of Mainstreaming Climate Resilience in WASH
04.
Understanding Climatology, Physical Parameters & Hazards
05.
Hazard & Investment Mapping
06.
Adaptation Options
Challenges we Encountered
07.
03.
CRA Process
Lessons Learnt
08.

## Slide 13: 01. Objectives of the CRA
        What is a Climate Risk Assessment ? What is the purpose of a Climate Risk Assessment ?
        Climate risk assessments identify the likelihood of future climate hazards and their potential impacts on communities. This is fundamental for informing the prioritization of climate action and investment in adaptation.
        In this case the CRA informed CWSSIP to ensure investment planning ensures adaptation through:
        Climate proofing of investments
        Due consideration of climate change when choosing investments location

## Slide 14: 02. Benefits of Mainstreaming Climate Resilience in WASH
Reduces operation and maintenance costs of water and sanitation infrastructure by minimizing climate-related damage and failures.
Improves efficiency in the use of financial resources, allowing savings to be redirected toward service expansion and increased coverage.
Promotes the development of durable, climate-resilient WASH infrastructure that can reliably serve current and future generations.

## Slide 15: 03. CRA Process
CRA steps
          STEP 1) Understanding the climatology and physical parameters
          STEP 2) Identifying hazards and exposure to it
          Consider past events and current exposure
          Account for climate change impacts on exposure
          STEP 3) Understanding vulnerability to hazards to which the County is exposed
          Especially WSS sectoral vulnerability
          Social and sectoral vulnerability
      Human Health
      Agriculture
      Coastal zone
      Energy and infrastructure
      Ecosystems
      Disproportionately impacted groups
          Transversal : Mapping and analyzing each step

## Slide 16: 04. Understanding Climatology, Physical Parameters & Hazards
        Parameters & Hazards Associated to Climate Change
Water

## Slide 17: 04. Understanding Climatology, Physical Parameters & Hazards
Understanding existing risks & their evolution with climate change
          Current Climatology Historical trends Projections
Observed annual average precipitation (top) and mean surface air temperature in Tana River
Source : CCKP
Monthly climatology, 1991-2023; Tana River
Source : CCKP
Projections of average mean temperature under SSP5-8.5
Source : CCKP
Frequency, intensity, duration &
locale of occurrence

## Slide 18: Hazard Identified
Tana River
Floods:
  Heavy rainfall floods (All county)
  River floods (Tana River surroundings mainly)
  Rising water table floods (limited information to map this out – surroundings on Tana River)
Heat stress and droughts (all the county)
Coastal erosion (coastal area) and rustle erosion (all the county)
Soil and water salinity (coastal area and irrigated inland areas or one close to rivers)
Sand and dust storms (all the county)
Pest and diseases (all the county)

## Slide 19: Hazard Identified
Murang’a
Floods:
  Maragua & Kiharu – intakes submerged, high treatment costs, 20–40% households affected
Drought:
  Severe in Ithanga/Kakuzi – up to 50% households affected; long treks for water, crop loss.
Landslides
  Frequent in Kangema, Mathioya, Kigumo – 2025 landslide in Kangema killed 6, cut off 980 HHs.
Extreme Rainfall
  Ndaka-ini station recorded 1,355 mm (among Kenya’s highest seasonal totals).
Heat Stress:
  Outdoor workers & water pans/dams affected by evaporation and heat waves.

## Slide 20: Murang’a Temperature

## Slide 21: Murang’a Drought

## Slide 22: Landslides

## Slide 23: Land Use Cover Change

## Slide 24: Pluvial floods

## Slide 25: 05. Hazard & Investment Mapping
          Importance of Mapping
HAZARDS
INVESTMENTS

## Slide 26: 05. Hazard & Investment Mapping – Landslide hazard

## Slide 27: 06. Adaptation Options
Based on field visits, litterature review (good practices) and experts’ inputs adaptation options were identified at three levels:
Project Design
County Level – Programmes and Legislation
Community Level Adaptation Practices

## Slide 28
Climate hazard | Impacts on infrastructure & Service quality | Impacts on environment and water resources | Social impact | CWSSIPs investments concerned | Adaptation Measures
Drought | Cracking of Linings: (e.g. with clay) Poor Water Quality (Salinity) Water Shortage | Degradation of resource quality through reduced dilution of pollutants Reduced Water Levels - Lack of Recharge: Loss of biodiversity | Disruption of Livelihoods: - water for Irrigation, livestock or domestic use Water resource conflicts between communities Health Risks – disease outbreaks | Construction of Bilbil water pan project in Chewele ward Construction of a new dam, construction of a slt trap, construction of auxilliary works, construction of a draw-off system, construction of a perimeter fence and a VIP toilet | Design considerations – Deepening to increase depth to boost storage capacity while reducing evaporation exposure Desilting - reduce evaporation exposure. Planting trees along the banks of the water pan – provide shade cover
Intense and sudden rainfall, flooding | Submergence of Pump and Headwork's Damage: - failure of pumps and other electrical systems rendering out of service out of service Submergence of boreholes – Water Contamination Reduced Accessibility Increased Maintenance Costs | Aquifer Pollution and Recharge Issues Loss of Biodiversity | Community Displacement Loss of human lives Disease outbreak – : waterborne diseases – cholera, typhoid, dysentery | Construction of Kaniki water supply project in Galedertu SC- The construction works will involve hydrological survey at Kanini village, Drilling and equipping of 2No. Boreholes, 1No. 50cum capacity elevate steel water tank at Gurujo, HDPE PN12 Rising main from kaniki to Gurujo and 2No. Standard water kiosks (1no. Per village). | Elevated Borehole Platforms –raised concrete plinths to protect borehole headworks and pump systems from floodwaters. Solar-Powered Pumps – reduce reliance on diesel pumps (fossil fuel)
Landslides | ………. |  |  |  | 
          Water Supply Infrastructure Table

## Slide 29: 06. Adaptation Options – Design adaptation examples
Elevated Borehole Platforms
HDPE water supply pipes with electro-fused joints ensures a watertight system.
Solarization of boreholes
Elevated storage tank enables gravity-fed water distribution - minimizing maintenance costs
Concrete reinforced pit latrines
Construction of ladder-like steps at designated water collection points along the River Tana to facilitate safer an easier water fetching.
Building fitted with gutters to harvest rainwater
Reinforced concrete water pipe anchors
Underground water pipelines

## Slide 30: 06. Adaptation Options – Design adaptation examples
Elevated Borehole Platforms – Madogo Tana River
Solarization
Adaptation to water transportation over long distances - Wolestokocha
Elevated Water Tanks

## Slide 31: 06. Adaptation Options – Design adaptation examples
HDPE pipes anchored by reinforced concrete –Irate, Murang’a

## Slide 32: 06. Adaptation Options – Design adaptation examples
Relocated pipes running along River South Mathioya valley in Kiarathe with river crossing fitted with GI pipes from the joint chambers and firmly anchored by concrete reinforced anchors

## Slide 33: 06. Adaptation Options – Design adaptation examples
Operational sheets for each investments are generated based on their location and their related hazard exposure, it lists all the adaptation that could be relevant for the proposed investment.

## Slide 34: 06. Adaptation Options – Programmes and Legislation examples
Construction of WASH infrastructure:
  Drilling boreholes
  Construction of Water Pans and Dams
  Water Supply network extension
Maintenance of existing water infrastructure
Enforcing proper design of dams, water structures, ensure compliance of engineering design standards and regulations.
Prevention and sensitization against encroachment of riparian areas, slope management by advocating for terrace farming, agroforestry, afforestation and tree planting
County Government supplements community efforts by distributing water treatment agents such as Pur and Aqualam.

## Slide 35: 06. Adaptation Options – Programmes and Legislation examples
Adaptation goes beyond the infrastructure – it includes legislation and other programmes at county-led programmes
Slope Stabilization – Murang’a
Need for Slope Management – Terrace Farming Practices - Afforestation – Tree Planting

## Slide 36: 06. Adaptation Options – Programmes and Legislation examples
Agroforestry – Kiarathe, Murang’a
Slope Management - Afforestation – Tree Planting

## Slide 37: 06. Adaptation Options – Community level adaptation practices examples
Planting trees
Roof water harvesting
Soil conservation
Pastoralism
Planting drought resistant crops
Boiling of drinking and traditional water treatment

## Slide 38: 07. Challenges We Encountered
Absence of most WSP representatives limited accurate identification of investment locations, as counties could only provide general, non-specific site information.
Mixing technical officers and community representatives in joint discussions reduced community participation, as technical staff dominated the conversations.
Some counties did not nominate the intended CWSSIP technical officers, necessitating additional training for backend teams to ensure continuity and institutional learning

## Slide 39: 08. Lessons Learnt
Active participation of Water Service Provider (WSP) representatives was critical as they implement most CWSSIP projects for some counties. Their involvement improves the accuracy of hotspot identification and investment locations.
Mapping investment locations was essential for identifying site-specific adaptation measures aligned to the climate hazards affecting each locality.
Separating technical discussions from community consultations, while ensuring complementarity between the two, leads to more inclusive, practical, and actionable outcomes.
Counties that engaged GIS Officers, Climate Change Officers, and Water Officers showed stronger technical understanding and ownership. Future support should prioritize early and consistent involvement of all relevant technical staff

## Slide 40: Representative concentration pathways
Status quo or worse RCP 8.5. Assumes that emissions continue to rise throughout the century and leads to increase in temperature of 3.2- 4.5 °C
Slower mitigation scenario RCP 6.0 Assumes that emissions peak in approximately 2060 before slowly declining, leading to an increase in temperature of 2.0-3.7°C
Moderate mitigation scenario RCP 4.5. Assumes that emissions peak in approximately 2040 before slowly declining, leading to increase in temperature of 1.7- 3.2°C
Best case scenario RCP 2.6. Declining emissions from 2020 and go to zero by 2100, leading to increase in temperature of 0.9-2.3°C

## Slide 41: SHARED SOCIO-ECONOMIC PATHWAYS
SSP1: The sustainable and “green” pathway describes an increasingly sustainable world.
SSP2: The “Middle of the road” or medium pathway extrapolates the past and current global development into the future
SSP3: Regional rivalry. A revival of nationalism and regional conflicts pushes global issues into the background.
SSP4: Inequality. The chasm between globally cooperating developed societies and those stalling at a lower developmental stage with low income and a low level of education is widening.
SSP5: Fossil-fueled Development. Global markets are increasingly integrated, leading to innovations and technological progress.
Notes: SSP1: The sustainable and “green” pathway describes an increasingly sustainable world. Global commons are being preserved; the limits of nature are being respected. The focus is more on human well-being than on economic growth. Income inequalities between states and within states are being reduced. Consumption is oriented towards minimizing material resources and energy usage.
SSP2: The “Middle of the road” or medium pathway extrapolates the past and current global development into the future. Income trends in different countries are diverging significantly. There is certain cooperation between states, but it is barely expanded. Global population growth is moderate, leveling off in the second half of the century. Environmental systems are facing a certain degradation.
SSP3: Regional rivalry. A revival of nationalism and regional conflicts pushes global issues into the background. Policies increasingly focus on questions of national and regional security. Investments in education and technological development are decreasing. Inequality is rising. Some regions suffer drastic environmental damage.
SSP4: Inequality. The chasm between globally cooperating developed societies and those stalling at a lower developmental stage with low income and a low level of education is widening. Environmental policies are successful in tackling local problems in some regions but not in others.
SSP5: Fossil-fueled Development. Global markets are increasingly integrated, leading to innovations and technological progress. The social and economic development, however, is based on an intensified exploitation of fossil fuel resources with a high percentage of the coal and an energy-intensive lifestyle worldwide. The world economy is growing, and local environmental problems such as air pollution are being tackled successfully.

## Slide 42
Step 01 | Assess hazards
Identify the probability, intensity and timescale of current and future climate hazards.
Climate Resilience Assessment steps
Example: Mombasa (using Climate Change Knowledge Portal)
          Projections
The data can be presented in two ways (Calculation selection in the filters):
Ensemble anomaly: this shows the projected change relative to a historical period for each month. This is the most correct scientific way of understanding multi-model changes.
Absolute projected climate variable (mean): this displays the actual projected value of the climate variable, covering both the historical period and extending into the future.
STEP 1: ASSESS HAZARDS
Notes: Facilitators notes:
This slide is a demonstration slide showing participants how to access future climate projections within the CCKP, which completes the Step 1 assessment.
Guide participants on navigating the CCKP to select climate projection parameters and differentiate between the two output options: Anomaly and Absolute Mean.

## Slide 43
Step 01 | Assess hazards
Identify the probability, intensity and timescale of current and future climate hazards.
Climate Resilience Assessment steps
Example: Mombasa (using Climate Change Knowledge Portal)
          Projections
STEP 1: ASSESS HAZARDS
Notes: Facilitators notes:
This set of charts represents the culmination of Step 1—the future projections using the 'Ensemble Anomaly' method we just discussed.
Remember, the Y-axis shows the change (anomaly) relative to the 1985-2014 baseline. The red shaded area represents the uncertainty across different climate models.

## Slide 44
Step 01 | Assess hazards
Identify the probability, intensity and timescale of current and future climate hazards.
Climate Resilience Assessment steps
Example: Mombasa (using Climate Change Knowledge Portal)
          Projections
Flood risk
  Precipitation is projected to increase in traditionally drier periods: January–March and the short rains (Oct–Dec)
STEP 1: ASSESS HAZARDS
Notes: Facilitators notes:
This slide is a summary slide, synthesizing the complex charts from the previous slide into three clear, actionable risk statements (the "Triple Threat").
Future climate projections indicate a significant and harmful shift, presenting a triple threat to Mombasa:
Heat Risk
  Warming trend: average maximum temperatures are projected to increase by up to +1.7 °C (peaking in July), with the overall mean rising by about +1.4°C.
  Extended exposure: the number of hot days (T-max>30 ∘ C) increases dramatically in the transition months—by up to +12 days in April/May and +14 days in October/November. This extends the window for severe thermal stress and contributes to a sharp peak in temperature-related excess mortality during the traditional hot season (January to March).

## Slide 45
          Tools for screening:
          ThinkHazard!
1) Enter location
2) Get a global screening
4) Select hazard for details
3) Download the whole PDF for analysis
By clicking on your county you can refine the area of study
The example of Mombasa (refine the analysis with ThinkHazard!)
STEP 1: ASSESS HAZARDS
Notes: Facilitators notes:
The objective of this slide is to illustrate the effective use of ThinkHazard for identifying, retrieving, and documenting the county's specific hazard exposure.
Briefly point out the main steps on the screen.

## Slide 46
The example of Mombasa (refine the analysis with ThinkHazard!)
STEP 1: ASSESS HAZARDS
Notes: Facilitators notes:
Here we have the example for Mombasa County, showing the different hazards to which the county is exposed, as well as the risk level for each hazard.

## Slide 47
Report the climate hazards identified in the Excel file Climate adaptation matrix
STEP 1: ASSESS HAZARDS
Notes: Facilitators notes:
This slide is a pivotal transition. It moves the participants from the theoretical hazard assessment to the practical application tool (the matrix).
Introduce the Climate Adaptation Matrix as the structure for synthesizing all findings and demonstrate how the hazards identified populate the matrix.
The first thing to do is to mention the different hazards you have identified after analyzing the risks and their evolution in the 'Climate Hazard' column.

## Slide 48
Step 01 | Assess hazards
report the county's exposure.
Climate Resilience Assessment steps
          1) Report exposure of the County
High | Medium | Low | NA
Notes: Facilitators notes:
Next, for each hazard recorded in the file, the corresponding risk level (colour-coded) is filled in as well. The task is to report the county’s overall exposure level for the relevant hazards.
Step 1 is now fully complete, and the data is mapped to the matrix. We have the Hazard. Now we must assess the vulnerability and hazard consequences. Let's move to Step 2

## Slide 49
Step 02 | Vulnerability assessment
Assessing infrastructure system vulnerability and hazard consequences
Climate Resilience Assessment steps
Notes: Facilitators notes:
Clearly mark the transition from assessing external threats (Hazards) to assessing internal fragility and consequences (vulnerability).

## Slide 50
STEP 2: VULNERABILITY ASSESSMENT
Don't forget to also assess the impact on women, young people, children, people with disabilities, the elderly, etc.
Notes: Facilitators notes:
Guide participants through the pre-populated matrix to illustrate the depth of analysis required for Step 2 and reinforce the relationship between hazards and consequences across sectors.
We now connect the hazards (from step 1) to their consequences across four crucial categories." (Point to the circled column headers: Impacts on infrastructure & service quality, Impacts on environment and water resources, Cross sectoral impacts, Social impacts).
The key lesson from step 2 is that climate impacts are complex and multi-sectoral. You must track effects from the pipe (infrastructure) to the patient (social impact) to complete a robust assessment.

## Slide 51
STEP 2: VULNERABILITY ASSESSMENT
Climate hazard | Impacts on infrastructure & Service quality | Impacts on environment and water resources | Social impact
Droughts, water shortage | Mouvement and damage of infrastructure related to changes in soil moisture levels | Degradation of resource quality through reduced dilution of pollutants | Reduced water for irrigation which may lead in increased wastewater use, and use of polluted receiving waters. Les water to clean toilets which can become unsanitary
Heat wave | Dysfunction of biological treatment processes (mortality of certain bacteria). (Ideal WW treatment temperature range being [20 - 35°C] not exceeding 40°C / WHO's recommendation for maximum drinking water temperature at the tap is 25°C) Heat-induced degradation of infrastructure and equipment. Degradation of concrete due to increased production of hydrogen sulfide2 (H2S) | Degradation of quality of resources through less well treated discharge | Poisoning from inhalation of hydrogen sulfide (H2S), which is produced more frequently by heat (safety risk for personnel, especially sewage workers). Odour nuisance due to increased nitrogen dioxide (N2O) emissions
Intense and sudden rainfall, flooding | Submergence failure of pumps and other electrical systems treatment plants treatment plants, rendering out of service out of service Septic tanks filling and backing up; backing up of sewers Fragilization and destruction of installations sewers: (scouring or washout of bedding, and flotation leading to cracking of the sewer pipes) septic tanks flotation destruction of latrines not built to sustain such hazards (impact on on access rates may be be significant) Disruption of emptying services (difficulty access, necessary increase in frequency...) | Increase of untreated water in the natural environment due to penetration of rainwater into the wastewater network causing overflowing, saturation of pumps and bypass at wastewater treatment plants Reduction of poluttants loads and resuspension, leading to difficulties in treatment process Treatment process dysfunction (hydraulic overload) Mixed flow wastewater and rainwater on public roads as a result of flooding of latrine and toilet pits, with consequent consequent health risks Inundation of soakaway or pit from below, increased potential for contamination of groundwater. | Population without sanitary sanitary facilities Increase in water-borne diseases due to the risk of contact with water containing pathogens
Storms (including sand and dust storms) |  |  | 
          Example of Sanitation Table
Notes: Facilitators notes:
This table provides a specific example for the sanitation sector to show how detailed this analysis needs to be.

## Slide 52
Step 02 | Vulnerability assessment
Assessing infrastructure system vulnerability and hazard consequences
Climate Resilience Assessment steps
Climate hazard | Impacts on infrastructure & Service quality | CWSSIPs investments concerned | Social impact
Droughts, water shortage | Mouvement and damage of infrastructure related to changes in soil moisture levels |  | 
Heat wave | Dysfunction of biological treatment processes (mortality of certain bacteria). (Ideal WW treatment temperature range being [20 - 35°C] not exceeding 40°C / WHO's recommendation for maximum drinking water temperature at the tap is 25°C) Heat-induced degradation of infrastructure and equipment. Degradation of concrete due to increased production of hydrogen sulfide2 (H2S) |  | 
Intense and sudden rainfall, flooding | Submergence failure of pumps and other electrical systems treatment plants treatment plants, rendering out of service out of service Septic tanks filling and backing up; backing up of sewers Fragilization and destruction of installations sewers: (scouring or washout of bedding, and flotation leading to cracking of the sewer pipes) septic tanks flotation destruction of latrines not built to sustain such hazards (impact on on access rates may be be significant) Disruption of emptying services (difficulty access, necessary increase in frequency...) |  | 
Storms (including sand and dust storms) |  |  | 
          Detail which infrastructures of the CWSSIP are concerned
Notes: Facilitators notes:
Knowing what is the exposure and the potential impacts of the hazard, we can tell which infrastructures are at risk
This is a critical step in the process. When we talk about "resilience building options," we're not just brainstorming a few ideas; we're developing a comprehensive long list of adaptation options to ensure the CWSSIP (County Water and Sanitation Strategy and Investment Plan) is robust against future climate shocks.
To do this effectively, we need to focus on two key areas:
Detailing affected infrastructure: we must identify exactly which components of the CWSSIP are most vulnerable to climate risks like floods, droughts, or extreme weather.
Developing measures (next slide): this involves creating specific climate-proofing and mitigation measures for each identified vulnerability. Climate-proofing means making the infrastructure itself resistant to climate impacts (e.g., using more durable materials or elevating critical equipment).

## Slide 53
Step 03 | Climate proofing
Ensuring long-term resilience of infrastructure systems against projected climate change hazards and their associated impacts
Climate Resilience Assessment steps
Notes: Facilitators notes:
Announce the final step: "We now move to Step 3: Climate proofing. This is where we ensure the long-term resilience of the system."

## Slide 54
Step 03 | Climate proofing
Ensuring long-term resilience of infrastructure systems against projected climate change hazards and their associated impacts
Climate resilience assessment steps
CWSSIPs investments concerned | Climate proofing
          Develop climate proofing and mitigation measures
Notes: Facilitators notes:
This slide is the culmination of the Climate Adaptation Matrix, illustrating where the adaptation measures are formally documented.
This is where you document the specific, actionable interventions. For every high-vulnerability consequence, you must propose a measure: e.g., if the risk is 'flood submergence of
pump stations,' the measure is 'elevate pump station above the 100-year flood line'

## Slide 55
Climate resilience assessment steps
Key questions and considerations.
How might the structural integrity, materials, longevity, and overall effectiveness of project investments be impacted by climate change and disasters?
How might climate change impact water infrastructure through extreme precipitation and floods?
How might gradual changes in seasonal or annual patterns of temperature, solar radiation, and drought impact the physical assets of the project?
What are the implications of climate and disaster impacts to project beneficiaries and stakeholders?
How should strategic plans, engineering design, implementation, operation and maintenance of water infrastructure consider the impacts of climate change and natural disasters as well as impacts by other sectors on the surrounding watershed?
Step 03 | Climate proofing
Ensuring long-term resilience of infrastructure systems against projected climate change hazards and their associated impacts
Notes: Facilitators notes:
Use the provided questions to guide the discussion from technical risks to human impact and final action. Begin with the physical threats to the infrastructure itself, challenging design standards and highlighting both extreme and gradual climate impacts. The goal is to make the risks concrete.
Then, pivot to the consequences of failure, focusing on how communities are affected and whether the design locks them into a vulnerable future. End by synthesizing this into a call for integrated action, emphasizing that climate resilience must be embedded across the entire project lifecycle—from initial planning through to long-term operation and maintenance.

## Slide 56
04 | Case study
Notes: Facilitators notes:
Clearly announce the start of the practical case study.

## Slide 57
Case study – climate First tool
Notes: Facilitators notes:
Let's dive into a case study.
The Adaptation Matrix is the essential starting point. It's the filter that determines where you spend your time and resources on detailed, costly engineering and economic studies.
We'll use ClimateFIRST—a quantitative tool for detailed assessment—to analyze an Anaerobic Baffled Reactor, demonstrating a deeper approach to engineering and financial
analysis

## Slide 58
Case study – climate First tool
An example of a completed ClimateFIRST assessment for an Anaerobic Baffled Reactor (ABR)
  https://utsd8.prod.acquia-sites.com/sites/default/files/2023-10/ClimateFIRST_ABR_0.xlsx
Notes: Facilitators notes:
Encourage participants to download and explore this file later. It serves as the target output—the level of detail the full resilience assessment should achieve.

## Slide 59
Case study – climate First tool
Notes: Facilitators notes:
Introduce the systematic five-step framework of the ClimateFIRST tool and its purpose: improving the resilience of sanitation technologies through detailed design analysis.
This concludes our review of the practical tools and case studies.
It’s time for lunch break.

## Slide 60
LUNCH
Notes: Facilitators notes:
Lunch break.
When we return, we'll shift from technical tools to a more strategic planning mindset.

## Slide 61
05 | What is scenario-based planning?
Notes: Facilitators notes:
This slide is a section break for the final content block of the day, signaling a major thematic shift toward strategic, future-focused planning.
Direct attention to the flood image. "This image shows the consequence of inadequate planning. Scenario-based planning is how we avoid this—it is about anticipating multiple possible futures, not just one."

## Slide 62
Definition
Scenario-based planning is a practical approach that you can use to improve and adapt your existing WASH planning to take account of climate change and other sources of risk and uncertainty.
  Shifts focus from predicting the future to preparing for different possible futures.
  It's flexible: can be used for a full multi-stakeholder plan or to adjust existing processes.
  Key benefit: develops climate-resilient strategies.
Image credit: nps.gouv
Extreme heat
Flood
Landslide
Wildfire
Notes: Facilitators notes:
Define scenario-based planning as a flexible approach to uncertainty and emphasize its key benefit: shifting focus from predicting one future to preparing for multiple possible futures.
Forecast Planning (Bottom Left): Traditional planning assumes one likely path (a single forecast). This leads to systems optimized for one future, which are brittle when that future doesn't happen.
Scenario-Based Adaptation (Bottom Right): "This shifts the focus. We don't try to predict; we prepare for different possible futures (the hazards shown: Wildfire, Extreme Heat, Flood). It builds flexibility and robustness.

## Slide 63
Photo by Genevieve French, Greenpeace
Beyond traditional planning: the case for scenario-based planning in WASH
Why move beyond traditional planning?
  Assumption of continuity: traditional approaches tend to assume that existing trends (e.g., in climate, population growth) will continue into the future.
  Focus on a single solution: they focus on finding one best solution to achieve an objective (such as 100% population with access to improved water or sanitation).
  Too simplistic: extrapolating current trends is too simplistic, which is often unreliable in a complex, changing world.
  Blind to risk: this approach is unlikely to capture the emerging risks presented by climate change or consider many possible solutions.
Why should scenario-based planning be of interest to WASH sector professionals?
  The challenge: we don't know the context or environment we will be operating in in the future.
  The goal: to improve and adapt existing WASH planning to take account of climate change and other sources of risk and uncertainty.
  The methodology: scenario-based planning is a practical approach to tackle these challenges.
Notes: Facilitators notes:
This slide provides the rationale for the shift from traditional planning to scenario-based planning, specifically targeting WASH sector professionals.

## Slide 65: Representative concentration pathways
Status quo or worse RCP 8.5. Assumes that emissions continue to rise throughout the century and leads to increase in temperature of 3.2- 4.5 °C
Slower mitigation scenario RCP 6.0 Assumes that emissions peak in approximately 2060 before slowly declining, leading to an increase in temperature of 2.0-3.7°C
Moderate mitigation scenario RCP 4.5. Assumes that emissions peak in approximately 2040 before slowly declining, leading to increase in temperature of 1.7- 3.2°C
Best case scenario RCP 2.6. Declining emissions from 2020 and go to zero by 2100, leading to increase in temperature of 0.9-2.3°C

## Slide 66: SHARED SOCIO-ECONOMIC PATHWAYS
SSP1: The sustainable and “green” pathway describes an increasingly sustainable world.
SSP2: The “Middle of the road” or medium pathway extrapolates the past and current global development into the future
SSP3: Regional rivalry. A revival of nationalism and regional conflicts pushes global issues into the background.
SSP4: Inequality. The chasm between globally cooperating developed societies and those stalling at a lower developmental stage with low income and a low level of education is widening.
SSP5: Fossil-fueled Development. Global markets are increasingly integrated, leading to innovations and technological progress.
Notes: SSP1: The sustainable and “green” pathway describes an increasingly sustainable world. Global commons are being preserved; the limits of nature are being respected. The focus is more on human well-being than on economic growth. Income inequalities between states and within states are being reduced. Consumption is oriented towards minimizing material resources and energy usage.
SSP2: The “Middle of the road” or medium pathway extrapolates the past and current global development into the future. Income trends in different countries are diverging significantly. There is certain cooperation between states, but it is barely expanded. Global population growth is moderate, leveling off in the second half of the century. Environmental systems are facing a certain degradation.
SSP3: Regional rivalry. A revival of nationalism and regional conflicts pushes global issues into the background. Policies increasingly focus on questions of national and regional security. Investments in education and technological development are decreasing. Inequality is rising. Some regions suffer drastic environmental damage.
SSP4: Inequality. The chasm between globally cooperating developed societies and those stalling at a lower developmental stage with low income and a low level of education is widening. Environmental policies are successful in tackling local problems in some regions but not in others.
SSP5: Fossil-fueled Development. Global markets are increasingly integrated, leading to innovations and technological progress. The social and economic development, however, is based on an intensified exploitation of fossil fuel resources with a high percentage of the coal and an energy-intensive lifestyle worldwide. The world economy is growing, and local environmental problems such as air pollution are being tackled successfully.

## Slide 67
The example of Mombasa (using the Climate Change Knowledge Portal)
STEP 1: ASSESS HAZARDS
Notes: Facilitators notes:
Look at the other options on the CCKP—things like geophysical and human dimensions.
These geophysical and human data layers are critical because they help us understand the exposure of assets and the vulnerability of communities, which completes the risk equation alongside the climate hazards.
Coastal flooding: the low elevation makes the area extremely vulnerable to storm surges, high tides, and future sea-level rise.
Fluvial/urban flooding: water has more difficulty draining on flat terrain, increasing the risk of stagnation flooding and insufficient drainage during heavy rainfall events.

## Slide 68
Main Steps of a CRA
Dhaka; Photo by Michael Foley, Flickr
1
2
3
4
5
6
Step 01 | Establish the decision-making context. What are the objectives of the CRA? What decision is to be made? Set the scope.
Step 02 | Assess hazards
Identify the probability, intensity and timescale of current and future climate hazards.
Step 03 | Assess impact
What are the potential impacts of those hazards on people, assets, services and the environment? Includes analysis of exposure, sensitivity and adaptive capacity.
Step 04 | Identify and Assess risks. Determine risks based on the likelihood of a hazard occurring and the consequence of the identified impacts.
Step 05 | Identify resilience building options
Determine a long list of adaptation options.
Step 06 | Appraise resilience building options. Assess options against decision-making criteria; prioritize resilience options.
Notes: Trainer Notes:
The following slides go over the main steps involved in conducting a CRA. The aim here is for participants to understand the overall process and steps of a CRA. Participants are not expected to be able to conduct a CRA, but they should have a basic understanding of its process and components. This can enable them to procure and supervise a CRA from an external consultant or organisation in the future.
This slide outlines the overall steps to conduct a CRA. Please note to participants that we have provided a generalised set of steps. Some methodologies will have slightly different names for the steps, or they may combine some of these steps into a single step (meaning those methodologies might have 5 steps instead of 6). Overall, the content in this section should provide a generalised approach that participants can follow and tailor to their own context.
The main steps of a CRA are:
Establish the decision-making context – this determines the scope of the CRA
Assess hazards: identify the probability, intensity and timescale of current and future climate hazards in a city.
Assess impact (threats and opportunities): describe the potential impacts of those hazards on people, assets, services and the environment. Includes analysis of exposure, sensitivity and adaptive capacity.
Identify and assess risks: determine the risks based on the likelihood of a hazard occurring and the consequence of the identified impacts. Involves ‘overlaying’ climate scenarios on the results of the previous two steps. This can involve a qualitative and/or quantitative assessment.
Identify adaptation/resilience building actions
Appraise or prioritise adaptation/resilience building actions (not covered in this course)
Following a CRA, the city would decide on which priority actions to implement, allocate funding for these initiatives, deliver them, and and monitor results over time. Implementation and monitoring should eventually feed back into risk assessment. Risk assessments should be updated over time as new information becomes available.

## Slide 69
Discussion
Which stakeholders would you gather around the table to define potential scenarios ?
Notes: Facilitators notes:
Facilitate a critical discussion on the crucial, often political, step of stakeholder identification and engagement required to successfully execute the Visioning and Scenario Building phases.

## Slide 70: Exercise
Download the Excel
Select second tab – adaptation
Select those for your hazard (one per table)
On a flipchart write:
Two adaptations you are comfortable with
Three that are new/are uncomfortable with
One that is NOT on the list

## Slide 71
07 | A quiz & end of the day reflection
Photo by Juan Davila on Unsplash
Notes: Facilitators notes:
This slide marks the conclusion of the training content, transitioning into a final assessment and wrap-up session.

## Slide 72: A quiz: Water and Sanitation Infrastructure Planning
What is an advantage of scenario-based planning? A) It guarantees a single certain future. B) It reduces the need for data. C) It allows for developing robust strategies in the face of uncertainty. D) It avoids any risk-taking.
Notes: Facilitators notes:
Each module ends with a short quiz of 3-4 questions for participants to check their understand.
Correct answer: C

## Slide 73: A quiz: Water and Sanitation Infrastructure Planning
Which Representative Concentration Pathway (RCP) represents the "worst-case" or "status quo" scenario, assuming that emissions continue to rise throughout the century and lead to a temperature increase of 3.2–4.5°C?
A) RCP 2.6
B) RCP 4.5
C) RCP 6.0
D) RCP 8.5
Notes: Facilitators notes:
Each module ends with a short quiz of 3-4 questions for participants to check their understand.
Correct answer: D) RCP 8.5

## Slide 74: A quiz: Water and Sanitation Infrastructure Planning
The example of Mombasa has shown that its low elevation (flat coastal terrain) exacerbates two major climate risks: coastal flooding and urban/river flooding.
This fact illustrates the role of which parameter in the CRA?
A) Topography
B) Winds
C) Precipitation
D) Temperature
Notes: Facilitators notes:
Each module ends with a short quiz of 3-4 questions for participants to check their understand.
Correct answer: A

## Slide 75: A quiz: Water and Sanitation Infrastructure Planning
Which tool allows for rapid screening of natural hazards? A) CCKP B) ThinkHazard! C) Google Maps D) Excel
Notes: Facilitators notes:
Each module ends with a short quiz of 3-4 questions for participants to check their understand.
Correct answer: B

## Slide 76: A quiz: Water and Sanitation Infrastructure Planning
What does the "Climate Adaptation Matrix" tool primarily help to do?
A) Calculate the carbon footprint of a project B) Design new climate models from scratch C) Climate-proof WASH investments by highlighting impacts D) Schedule maintenance for water treatment plants
Notes: Facilitators notes:
Each module ends with a short quiz of 3-4 questions for participants to check their understand.
Correct answer: C

## Slide 77: Highlights from module 5 'Toolkit for Water and Sanitation Infrastructure Planning'
This final module provided practical tools for planning and stress-testing infrastructure under climate uncertainty. It introduced scenario-based planning, which helps anticipate multiple possible futures rather than relying on historical data. This approach supports flexible and adaptive strategies for resilience.
We discussed how to differentiate between hard infrastructure (physical assets) and soft infrastructure (institutional systems) and understand cascading failure risks. Tools such as the Climate Adaptation Matrix and ClimateFIRST were presented for assessing vulnerabilities and identifying adaptation options.
The module concluded by discussing tendering climate risk assessments and integrating technical and institutional measures into adaptation strategies. By applying these tools, you can climate-proof WASH investments and ensure systemic resilience rather than focusing on individual assets.
Notes: Facilitators notes:
Summary of this module.

## Slide 78
Summary of key points
• The implementation of a structured planning process is essential to ensure that infrastructure remains resilient and effective for the long term in the face of climate uncertainty.
• Powerful tools like CCKP and ThinkHazard! should be leveraged to conduct robust climate risk assessments and inform data-driven adaptation strategies.
• A comprehensive risk management approach involves the systematic identification of climate hazards, the evaluation of their potential impacts, and the prioritisation of the most critical risks.
• Robust adaptation strategies are developed by integrating a combination of "hard" physical structures and "soft" policy-based or non-structural solutions.
Notes: Overview of key points of this module

## Slide 79
Summary of key points
• A strategic shift from traditional planning to dynamic, scenario-based planning is necessary to prepare for and anticipate multiple possible futures.
• Adaptive management should be embraced as a continuous cycle of monitoring progress, learning from outcomes, and making informed adjustments to strategies.
• In data-scarce contexts, pragmatic and informed decisions can still be made by effectively working with the best available data and leveraging local knowledge.
• Strengthening long-term resilience requires empowering local stakeholders through capacity building and fostering a sense of ownership over climate assessment tools and processes.
• Gender equality, youth engagement, and planning based on disaggregated data are essential for resilient and inclusive infrastructure.
Notes: Overview of key points of this module

## Slide 80: Extra resources Module 5
The Adaptation Principles: 6 Ways to Build Resilience to Climate Change
CLIMATE RESILIENCE SUPPORT FOR KENYA WATER, SANITATION, AND HYGIENE PROGRAM (K-WASH): Climate Risk Assessment (CRA) presentation to Counties by groupe huit
University of Technology Sydney: https://www.uts.edu.au/
Adaptation Principles : A Guide for Designing Strategies for Climate Change Adaptation and Resilience cb | UNDP Climate Change Adaptation by UNDP
https://climatescreeningtools.worldbank.org/sites/default/files/inline-files/CDRS%20Reference%20Guide%20Water_0.pdf by World Bank Group
ThinkHazard!: http://thinkhazard.org - For initial hazard screening.
Climate Change Knowledge Portal (CCKP) - World Bank: https://climateknowledgeportal.worldbank.org - For climate data and projections.
https://www.fisheries.noaa.gov/national/climate/scenario-planning-tool-climate-informed-decision-making
https://www.nps.gov/subjects/climatechange/scenarioplanning.htm
https://www.nps.gov/subjects/climatechange/upload/Scenario-Workshop-APIS-508compliant.pdf
https://www.environment.gov.rw/index.php?eID=dumpFile&t=f&f=55461&token=9b346eec57470d41931161671509c7459f78ed55
Notes: Facilitators notes:
This slide provides an overview of the key materials underlying Module 5

## Slide 81: End of day reflection
Yellow post-it what went well today
Pink post-it what could be improved of today
Post them on the evaluation sheet when leaving the room
Notes: Facilitators notes:
End of the day reflection.
Ask participants to write down I their facilitators handbook
What went well?
What needs to be improved on both content and learning techniques?
Things that they want to remember for rolling out the training
Ask participants to share their reflections in plenary.